## Slide 1: NHD and the Open Water Data Infrastructure
Al Rea
ahrea@usgs.gov

## Slide 2
What is the National Hydrography Dataset?
Essentially the surface water features found on topographic maps

## Slide 3
The fundamental component is the drainage network of rivers and streams
7.5-million mile network

## Slide 4
Completing the network through waterbodies

## Slide 5
Completing the network through waterbodies
with artificial paths
6.5 million waterbodies

## Slide 6
Attributes provide basic intelligence
Swan Creek
Perennial
Intermittent
Ephemeral

## Slide 7
Flow Direction – A key piece of intelligence

## Slide 8
Navigation – The basis for analysis

## Slide 9
Reach
14010002000421
Reach
14010002003345
Linear Referencing – Stream “Reaches”

## Slide 10
100
0
50
75
25
14010002000421
Linear Referencing – Stream addresses

## Slide 11
USGS Streamgage
09050000
Address:
Reach – 14010002000421
Measure – 19.8392
Coordinate
106 05 13.955 W
39 32 43.472 N
Linear Referencing – Data “Events”

## Slide 12
Connecting the streamgage to the network
Streamgage
Dam
Blue River
Artificial Path
(Blue River)
Green Mountain
Reservoir
Downstream
Upstream
Notes: Linking events to the NHD makes the NHD more intelligent. The streamgage makes the network more intelligent and the network makes the streamgage more intelligent. We know that upstream of the streamgage there is a dam, with regulated flow, we know all about the dam – who runs it, its construction material, its height, how many acre-feet it can hold, etc.; we know there is a reservoir behind the dam, we know its name, we know its area, we know the spillway elevation; we know how many miles of stream flow into the streamgage, we know how many miles of that is perennial, intermittent, and ephemeral flowing streams; we know there is a diversion upstream diverting 300 cfs out of the basin and thus reducing the flow through the streamgage; we know there is a heavy metals tailings pond upstream; we know what fish species live upstream; we know the water chemistry at various points upstream; we know the names of all the streams and lakes upstream, and on and on.

## Slide 13
Adding geospatial context to streamflow data

## Slide 14
Dams and Streamgages Integrated with the NHD

## Slide 15
Gage
Diversions
Identifying diversions upstream of a streamgage
Easily accomplished with a good database and a GIS
Analyzing Relationships

## Slide 16: Common Hydrographic Frames of Reference
RF-1
  1:500,000 scale
  Developed in 1980’s
  National or large regional studies/models
Medium-Resolution NHD
  1:100,000 scale
  Completed 2001
  Basis of NHDPlus
  Regional studies/models
High-Resolution NHD
  Multi-scalar, 1:24,000 scale or better
  Nationally complete 2007
  Current maintenance, many improvements

## Slide 17
Notes: Note it is difficult to reference sites of interest that are on tributaries not represented in the stream network being used. Therefore a site on one of the green or blue streams would be difficult to reference to the red RF-1 streams. This is why it is better to reference things to the most detailed network available, then use generalization rules to determine how to represent the things being referenced if a more general network is desired.

## Slide 18
Elevation
Hydrologic Units
(HUC12)
Stream Network
NHDPlus provides a Surface Water Geospatial Framework
Stream Network | Map Scale | Map Accuracy | Total Stream Miles (mi) | # of Stream Segments | Stream Segment Average Length (mi) | # of Lakes | Catchment Average Area (sq mi)
Reach File Version 1 (RF1) | 1:500K | +/- 254m | 600,000 | 60,000 | 10 | 4,100 | 50
Medium Resolution NHD | 1:100k | +/- 50m | 3,200,000 | 2,600,000 | 1.2 | 38,000 | 1.1
High Resolution NHD | 1:24K or better | +/- 12m | 7,500,000 | 20,000,000 | 0.37 | 537,000 | do not exist
NHDPlus catchments link the landscape to the stream network forming a surface water geofabric

## Slide 19: EPA WATERS Data:
Public Access
Listed Impaired Waters
Assessed Waters
Beaches
Clean Watershed Needs
Combined Sewer Overflows
CWSRF Benefits Reporting
Permitted Dischargers
Fish Consumption Advisories
Fish Tissue Data
Impaired Waters with TMDLs
Sewage No Discharge Zones
Nonpoint Source Projects
Water Quality Standards
Water Quality Stations
Internal Access Only
Drinking Water Intakes
Source Water Areas
Special Appropriations Projects
~6,000,000 events tied to 100K NHD

## Slide 20: HR NHD Type 1, Gaging Station: 127,659

## Slide 21: HR NHD Type 6, Water Quality Station: 93,787

## Slide 22: HR NHD Type 2, Dam: 60,311

## Slide 23: Point Events in NHD March 4, 2014
Type |  | 
1 | Gaging station | 127,659
2 | Dam | 60,311
3 | Divergence Structure = General | 25
4 | Divergence Structure = Withdrawing | 1,236
5 | Divergence Structure = Contributing | 63
6 | Water Quality Station | 93,787
ALL |  | 283,081

## Slide 24: A Single Hydrographic Frame of Reference
Based on High-Res NHD
  Single addressing system
  Single dataset to maintain
High-Res NHDPlus
  Currently in development
  Network Value Added Attributes (VAA’s), catchments, rasters, flow estimates
Generalization scheme
  Several generalized scales based on High-Res NHD
  NHDPlus derivatives for each scale

## Slide 26: Existing web services (EPA WATERS NHDPlus 100K-based)
EPA WATERS Web and Database services
  Event indexing
  Point indexing
  Name service
  Navigation service
  Navigation delineation service
  RAD event info service
  Lookup services
  Results queue service
  Spatial assignment service

## Slide 27
Incremental
Cumulative

## Slide 28: HEM Web Initial Release
Release date – April 30th, 2014
  SOE
  HiRes NHD Read-Only Web Map Service (AGS)
    National Coverage
    Updated Daily
    Enables display/query and snapping
  Sample JavaScript API Code
  Configuration Documentation
  http://nhd.usgs.gov/tools.html#hem
  Contact: hem@usgs.gov

## Slide 29: Open Water Data Initiative
Kevin T. Gallagher
USGS, Associate Director, Core Science Systems
June 26, 2014
Steering Committee Meeting

## Slide 30: Open Water Data Vision
Foundational National Data Sets with Data Services to support a wide variety of water user applications
Water data metadata, web services and a community accessible on the Federal Geospatial Platform
Access to integrated real-time monitoring data
Data Assimilation for a National Modeling capability
Water Maps and other Derivative Products that integrate geospatial & water observations
  Such as: current conditions, precipitation estimates, reservoir storage
Marketplace of open source applications (models, data visualizations, etc.) built upon Open Water Web Services

## Slide 31: Foundational Water Data Sets
Streamflow
Groundwater levels
Aquifers
Water quality
Reservoir storage
Elevation
Hydrography – NHD/WBD
Landscape Variables
Climate/Weather/ET
Soil moisture
Human water use
  Withdrawals
  Return flows
  Diversions
  Losses

## Slide 32: ACWI – Advisory Committee on Water Information
Established in 1991
Notes: ACWI through its subcommittees, including the joint ACWI / FGDC committee on spatial water data, has long had the objective of more effectively sharing comparable water data across the federal water sector. Several significant capabilities now exist through ACWI that include water-quality and groundwater data portals with web services. These capabilities will be leveraged and integrated within the proposed architecture.

## Slide 33: Proposal
We are proposing an Open Water Data Initiative that will:
  integrate currently fragmented water information into a connected, national water data framework
  leverage existing shared infrastructure and tools to provide a platform for innovation, modeling, and data sharing and solution development.
  capitalize on cross-government interest in big data, IT innovation, Open Data, Data.gov, etc.
  Build on the ground-breaking work of the FGDC, OGC, IWRSS, CUASI, ACWI, and others.

## Slide 34: Charge for the FGDC
In collaboration with the ACWI and other partners – Advance an Open Water Data Initiative, including:
  Reviving and populating the joint Subcommittee on Spatial Water Data to design a national open water data infrastructure;
  Supporting IWRSS consortium members in the scoping and implementation pilot activities;
  Creating an integrated water data portfolio for specific hydrologic regions or basins;
  Developing a technical reference architecture that supports the sharing of water data and links observations to geospatial data;
  Leveraging the Geospatial Platform to make water data more accessible and to support water data community collaboration;

## Slide 35: Charge for the FGDC cont.
  Identifying how existing investments in water data sharing can be integrated and leveraged;
  Engaging the international community in standards and technology development including the Open Geospatial Consortium;
  Identifying and prioritizing improvements to relevant framework geospatial data (National Hydrographic Dataset, Watershed Boundary Dataset, National Elevation Dataset, National Geologic Map Database, and the National Cooperative Soil Survey);
  Utilizing the FGDC coordination and governance structure to support related activities in the federal water sector.

## Slide 36: Next Steps
Endorse revival and re-populating of Subcommittee on Spatial Water Data
Issue charge to the subcommittee
  Work with IWRSS consortium members to:
    Refine charge going forward
    Define and implement Pilot Projects
Schedule “periodic” check-ins with the Steering Committee

## Slide 37: Use Cases
NFIE
Short Term Networks/temporary gages (Marie Peppler)
Data from Sandy, other floods
  Project underway now
  Can exercise the services
  Main goal: NHD indexing (events)
  Secondary goal: navigation, event discovery
Hydro Geospatial Fabric/National Hydrology Model (Roland Viger)
West Virginia chemical spill

## Slide 38: West Virginia Chemical Spill
Spill one mile upstream from water treatment plant
Incident Command Tool for Drinking Water Protection (ICWater) used to warn downstream water suppliers
  Uses NHDPlus flows and velocities
  Adjusts with real-time gage data
  Provided accurate travel-time estimates
  Protected Cincinnati water supply and others

## Slide 39
Model velocity
Measured
velocity
Spill site
Intake

## Slide 40
Downstream trace
Spill site

## Slide 41: Intakes near Cincinnati
120 hours

## Slide 42: Potential Future NHD Services
Expose most/all data as features/related tables
Up/Downstream navigation with event discovery
Event clearinghouse(s)
  Open – federated catalog
  Service-based
  Discoverable
  Initial hosted community via ScienceBase
Event management services
  Event synchronization
  Event migration between scales

## Slide 43: What services are needed for NFIE?
Do WATERS services do everything needed?
    Event indexing
    Up/Downstream navigation?
    Others?
Does NFIE need to reference any network other than NHDPlus?
What supporting services are needed?
  WFS? Which features?
  WCS for elev?
  2D to 3D line service?

## Slide 44: What are recommended processes?
Scoping of pilots?
Development of standards?