## Slide 1
David K. Arctur, David R. Maidment
Center for Research in Water Resources
University of Texas at Austin
OGC Hydro DWG Annual Workshop
BRGM, Orleans France, 20-23 September 2015
This research is supported in part by NSF EarthCube grant 1343785
Comparison of National Geo-Fabrics:
USA, Canada, Australia, INSPIRE-Italy

## Slide 2: Motivation
HY_Features can provide a common information model for describing national hydrologic-geospatial frameworks, sometimes called geo-fabrics
    This could enable automated cross-border interoperability and database conversions for watersheds spanning adjacent countries in Europe, Latin America, Africa, etc.
However, the national geo-fabrics do not instantiate all the same concepts, so mapping between them can be problematic and lossy.
    HY_Features is not the cause of this issue, but could help document it

## Slide 3: Outline
This presentation focuses on selected core feature classes of 4 national geo-fabrics
      USA National Hydrographic Dataset (NHDPlus)
      Australia Hydrographic Geo-Fabric (AHGF)
      Canada National Hydrographic Network (NHN)
      European INSPIRE as implemented in Italy
These are based on sample ArcGIS geodatabases, representing a subset of the full specifications.
  We’ll compare these with each other, and with HY_Features

## Slide 4
USA National Hydrographic Dataset (NHDPlus)
Australia Hydrologic
Geo-Fabric (AHGF)
Canada National Hydrographic Network (NHN)
EU INSPIRE Hydrology: Italy Idrografia

## Slide 5
NHDPlus
AHGF
NHN
INSPIRE-Italy
Souris River Basin N. Dakota, USA
Southeast Coast
Australia
Mahoney Lake Basin NW. Canada
Po River Basin N. Italy

## Slide 6: Flowlines and Waterbodies
All four data models have flowlines and waterbodies
NHDPlus flowlines have reliable network topology
AHGFNetworkStreams have topology, but AHGFLinks and AHGFNodes have “contracted” topology which is stable and reliable, at a coarser scale than NetworkStreams
Notes: AHGF doesnt in fact have a "reach" implemented in the same sense as NHD. It has a DEM derived stream network - but these are not reliable (for many reasons) - they are artifacts of scale and processing, not necessarily hydrology. Contracted catchments are the highest level of granularity at which something equivalent makes sense, and these are far coarser than NHD.
Contracted catchments are really only available in the latest product for the Murray Darling and Tasmania. The rest is really just a slightly improved stream netowrk - and there are major problems with these too - not including channelised streams in the network for example!

## Slide 7
Flowline
AHGFNetworkStream
NHN_HN_PrimaryDirectedNLFlow
NHDPlus
AHGF
NHN
INSPIRE-Italy
hy-p:SurfaceWaterL
AHGFLink
AHGFNode

## Slide 8
Flowline
Waterbody
NHD_HD_Waterbody
NHN_HN_PrimaryDirectedNLFlow
NHDPlus
AHGF
NHN
INSPIRE-Italy
hy-p:SurfaceWaterS
hy-p:SurfaceWaterL
AHGFNetworkStream
AHGFLink
AHGFNode
AHGFWaterbody

## Slide 9: Catchments vs. Basins to a hydrologist
NHDPlus and AHGF have the concept Reach Catchment to mean the local drainage area of a single flowline.
NHDPlus uses the term Basin to mean a drainage area defined by human means like HUC units.
Catchment is considered to be a synonym of Basin.

## Slide 10
Flowline
Waterbody
Catchment
NHDPlus
AHGF
NHN
INSPIRE-Italy
No Reach-Catchments
No Reach-Catchments
AHGFContractedCatchment
AHGFCatchment
AHGFNetworkStream
AHGFLink
AHGFNode

## Slide 11
Basin
NCBLevel1DrainageDivision
NCBLevel2DrainageBasinGroup
NHN_Workunit_Limit_2
NHN_Index_15
(groups of Workunits)
NHDPlus
AHGF
NHN
INSPIRE-Italy
hy-p:DrainageBasinS
HUC Region 9
(all Basins)
HUC = Hydrologic Unit Code

## Slide 12: Relating a Catchment with its Reach
NHDPlus defines a unique catchment for every reach
    NHDPlus has a direct reference between each flowline and its catchment
      Catchment:FeatureID = Flowline:COMID

## Slide 13: Why Does This Matter?
Flood Forecasting:
    Requires workflow to convert precipitation forecasts to runoff and then to streamflow discharge
    Land Surface Models (LSM) such as ECMWF LIS and WRF-Hydro coupled with RAPID require catchment-to-flowline linkage
    It may be feasible to work with catchment-flowline connectivity through a shared junction, but direct reference between catchments and their reaches is simpler and performs better

## Slide 14: National Models vs. HY_Features

## Slide 15: Hydrologic Representations Vary
      Cartography and connectivity are two distinct types of representation in HY_Features
Relationships between network connectivity and cartographic representations vary by data product
    INSPIRE distinguishes SurfaceWater (cartographic point, curve, surface) from NetworkElement (point, curve, surface) features
    NHDPlus Flowlines and Catchments are both cartographic and topological
    AHGF has a DEM-derived stream network. Contracted nodes and catchments are a coarser view of this network, where the connectivity is stable and accurate (see notes)
Notes: AHGF doesnt in fact have a "reach" implemented in the same sense as NHD. It has a DEM derived stream network - but these are not reliable (for many reasons) - they are artifacts of scale and processing, not necessarily hydrology. Contracted catchments are the highest level of granularity at which something equivalent makes sense, and these are far coarser than NHD.
Contracted catchments are really only available in the latest product for the Murray Darling and Tasmania. The rest is really just a slightly improved stream netowrk - and there are major problems with these too - not including channelised streams in the network for example!

## Slide 16: Basins vs. Catchments in HY_Features
All four national models have a similar concept of a Basin as a spatial unit for reporting purposes.
    Typically organized around major river drainage areas
HY_Features distinguishes between arbitrary catchments (HY_Catchment) and catchments which are topologically connected by a stably-identified outflow (HY_Basin)
HY_Features allows multiple geometric representations for each catchment, eg, HY_CatchmentArea
NHDPlus Catchments would thus be described in terms of both HY_CatchmentArea and HY_Basin, for both geometric and flow concepts

## Slide 17: Automating Database Conversions
      One role of HY_Features could be to facilitate data model and database translations across national borders. This would be of great utility, such as supporting applications for countries that have not developed their own national data models
      INSPIRE countries may not need this at European-interior borders, but may benefit from mapping to non-INSPIRE countries
HY_Features was not considered initially for transforming physical databases, but for describing the relations between components of a data model, and between data models, in a machine-usable way
      By itself, HY_Features does not fix semantic mismatches between national data models, but helps make them explicit
      Better, more mature tools are needed to make physical data conversion productive, eg, to make up for lack of river catchment topology
      While GIS can create and maintain river topology very well, it does not link the topology with other feature types, which would be of use to more applications than just hydrology

## Slide 18: NHDPlus to HY_Features Mapping - 1
HYF2NHD-catchment-flowline-junction-RA.pdf

## Slide 19: NHDPlus to HY_Features Mapping - 2
HYF2NFIE-catchment-flowline-midpoint-streamgage.pdf

## Slide 20: GML / GIS Integration Challenges
Typical Complex GML Requirements
    Nested objects
    Series / list elements
    Multi-geometries / representations
    Unique ids needed for each level / geometry
    Many required elements not available from source
Result: Single GML object maps to many child records in multiple related tables

## Slide 21: GIS to GML: Feature Type Mappings in FME: NHDPlus to HY_Features
Some feature classes from the GIS database are described by more than one HY_Features class… this makes the meaning of each source feature class more explicit, but HY_Features is more like metadata about the GIS database model,
not another GIS database model itself…

## Slide 22: HY_Features GML Schemas (FME import)
Many properties of HY_Features schema are for lists of GML-related entities… what should be done with these?

## Slide 23: Conclusions: If we want to take flood forecasting global…
We need the concepts of reach-catchments and stream network connectivity to be generally available
    Some national models do not currently implement these
    HY_Features could be used to clearly & crisply describe river network connectivity for automated use where geometric topology networks have not been created
But HY_Features lacks tools & visualization to make mappings easily understood and automated
    Neo4J integration for fast river network connectivity
In the meantime, current GIS database mapping & processing tools can be used, eg, ArcGIS and FME

## Slide 24
David K. Arctur, David R. Maidment
Center for Research in Water Resources
University of Texas at Austin
Thanks!
Some work to do yet…