## Slide 1
David R. Maidment
Center for Research in Water Resources
University of Texas at Austin
Presentation to the OCG Hydrology Domain Working Group
Orleans, France, 22 September 2015
Acknowledgements: Fernando Salas, Marcelo Somos Valenzuela, David Gochis, Ed Clark,
Don Cline, Jack Dangermond, Andy Ernest, Richard Hooper
This research is supported in part by NSF EarthCube grant 1343785
National Flood Interoperability Experiment

## Slide 2: The Opportunity
New National Water Center established on the Tuscaloosa campus of University of Alabama by the National Weather Service and federal agency partners
Has a mission to assess hydrology in a new way at the continental scale for the United States

## Slide 3: Integrated Water Resources Science and Services (IWRSS)
Weather
Rivers
Impact
Data
Formal partnership across these four agencies

## Slide 4: NWS River Forecast Centers (RFCs)
  Prepare river and flood forecasts
  Provide forecast guidance to Weather Forecast Offices (WFOs)
  Issue daily stage and streamflow forecasts, and flash flood guidance
  Work with water managers and other Federal Agencies
4
6600 sub-basins in continental US
Notes: RFC Summary

## Slide 5
100 million people on coast
No River Forecast
Notes: THERE’S A MAJOR GEOGRAPHIC GAP – WE DON’T FORECAST ALONG THE COAST

## Slide 6
FY15 Centralized Water Forecasting
Centralized Data Archive – all RFC data
Modeling Testbed – new NWC capabilities
National Water Center
Notes: TRANSITION INTO METHODS
FY15 PROJECT HAS FOUR CORE COMPONENTS
RFC archive
Model evaluation service
Modeling testbed
Centralized modeling demonstration

## Slide 7: RFC Forecast Point: Onion Creek at Highway 183
USGS Gage 08159000
NWS Forecast Point ATIT2
National Flood Interoperability Experiment
Geospatial data framework for Texas
NFIE-Geo Texas
NHDPlus Catchment 5781369

## Slide 8: WaterML2 Observations from USGS and Forecasts from NWS for this location
USGS Observed Flows, July 19
NWS Forecast Flows, July 19-20
USGS Gage 08159000
NWS Forecast Point ATIT2
Past and Present
Future

## Slide 9
Inaugural Meeting – May, 2014

## Slide 10: Transformative Research (NSF)
Transformative research involves ideas, discoveries, or tools that radically change our understanding of an important existing scientific or engineering concept or educational practice or leads to the creation of a new paradigm or field of science, engineering, or education. Such research challenges current understanding or provides pathways to new frontiers.
http://www.nsf.gov/about/transformative_research/definition.jsp
How to move from evolutionary change
to transformative change?

## Slide 11: National Flood Interoperability Experiment (NFIE) (Sept 2014 to August 2015)
Partnership between NWS and the academic community (Interagency Agreement between NSF and NOAA)
Included a Summer Institute for 44 graduate students from 19 Universities at the National Water Center, June 1 to July 17, 2015

## Slide 12: Goal of the Experiment
Close the gap between National Flood Forecasting and Local Emergency Response
Demonstrate forecasting of flood impacts at “stream and street level”
National
Local
Weather and Hydrology
National Weather Service and federal agencies
National Water Center
River Flooding and Emergency Response
Local, State and Regional Agencies
Citizens

## Slide 13: NFIE Conceptual Framework
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Community Flood Response System

## Slide 14: Open Water Data Initiative (OWDI)
Subcommittee on Spatial Water Data leads this effort
Al Rea (USGS) and Ed Clark (NWS) are co-chairs
This reports to both FGDC and ACWI
Sponsoring a series of “experiments” with water information services
NFIE is one of these experiments
Chair
Anne Castle, Former Asst Secretary for Water and Science, Dept of Interior

## Slide 15: NHDPlus Version 2.1
National Elevation Dataset
National Hydrography Dataset
National Land Cover Dataset
Watershed Boundary Dataset
NHDPlus
Foundation for a Geospatial Hydrologic Framework for the United States
2.7 million reach catchments in US
average area 3 km2
reach length 2 km
Uniquely labelled

## Slide 16: Flood Information for Fritz Hughes Park Rd
National Hydrography Dataset Plus
catchment for Bear Creek
(area = 5.71 km2)
Low water crossing at
3400 Fritz Hughes Park Rd

## Slide 17
500,000 processors operating in parallel
Stampede
1.2 million gallon cooling tank

## Slide 18: WRF-Hydro Forecasting Model
Runoff
Streamflow
RAPID flow routing (for continental US)
Probabilistic flood forecasts
Weather model and forecasts (HRRR)
Land-Atmosphere Model (NOAH-MP)
Precipitation
Weather
Catchment-level forecasts
Computed for the continental US in 10 minutes at Texas Advanced Computing Center

## Slide 19
RAPID River Routing Model
River Application for Parallel ComputatIon of Discharge
Flow
Legend
Dam
Junction
Catchment
Computational Unit for Rivers
Forcing: Runoff and reservoir releases
http://rapid-hub.org/
NHDPlus Catchment
Sprism = KQ
Swedge = KX (I – Q)
Muskingum
Method

## Slide 20
Grid to
catchment
NHDPlus
to RAPID
Forcing
WRF-Hydro
HRRR
ECMWF
NFIE-Hydro
TACC

## Slide 21: Current and NFIE Forecast Systems
130 Catchments and Flowlines
uniquely labelled
Two basins and one forecast point
becomes
Current: 6600 basins and 3600 forecast points
NFIE: 2.7 million stream reaches and catchments
A national flow network
Blanco River at Wimberley
Basin ~ 400 Sq Mile
Reach Catchment ~ 1 Sq Mile

## Slide 22: Linear Referencing on Flowlines
Lat.
Long.
Measure
Bridge and Stream Gage at RR 12 is at Measure 70.246
on Flowline 1630223
Measure is the % distance upstream from most downstream point on line
Using measures, the flow can be estimated at any point along the line

## Slide 23: Basic Ideas
A
B
n1
n2
n3
A
Flowline A flows to Flowline B through node n2
Catchment A drains to Flowline A
Each flowline has attributes “from-node” and “to-node”
Objects are placed on flowlines using linear referencing
A catchment is receives runoff from
land-atmosphere cells

## Slide 24: Next Step: National Water Prediction Model Configurations
Short-Range
‘Flood Prediction’
Long Range
‘Water Resources’
Analysis & Assimilation
Hourly
3-Hourly
~Daily (x16)
- 3 hrs
Cycling Frequency
WRF-Hydro IOC Configurations – May 2016
0-2 days
0-30 days
Forecast Duration
1km/250m/NHDPlus Reach
1km/250m/NHDPlus Reach
1 km/catchment /NHDPlus Reach
Spatial Discretization & Routing
MRMS blend/ HRRR-NAM bkgnd.
Downscaled HRRR /RAP/NAM blend
Downscaled & bias-corrected CFS
Meteorological Forcing
Medium Range
‘Flow Prediction’
Daily
0-10 days
1km/250m/NHDPlus Reach
Short-range + Downscaled GFS

## Slide 25: Interest from China
Dear David, It's just a quick response to your enquiry about China's interest in your proposal. I confirm our interest in doing similar thing in China. And, I wish the similar system could be run in China National Forecast Center in near future. For the time being, we have the maps of land use, topography at scales of 30 or 90 meters, and the soil map is available at the grid size of 1km. To achieve the goal, I think your technical support is needed with thanks. With best regards, Zhiyu LIU
Vice-President of WMO Commission for Hydrology Director of Hydrological Forecasting Center, the Ministry of Water Resources.

## Slide 26: Conclusions
The National Flood Interoperability Experiment has been a significant success in rapidly prototyping a high spatial resolution flood forecasting system for the continental US
This is a “flow continuum” model on the national stream network, like atmospheric and ocean models
China and Australia have indicated an interest in doing something similar
NHDPlus provides the geospatial information foundation in the US
What can we propose for a comparable international framework? Flows don’t stop at the border
Initiate a Geospatial Interoperability Experiment?