## Slide 1: OM-JSON
Simon Cox | Research Scientist | Environmental Information Infrastructures
21st September 2015
Land and water, Data61
a JSON implementation of O&M
Peter Taylor | Engineer | Autonomous Systems

## Slide 2: O&M
OM_Observation
+
phenomenonTime
+
resultTime
+
validTime [0..1]
+
resultQuality [0..*]
+
parameter [0..*]
GF_PropertyType
GFI_Feature
OM_Process
Any
+observedProperty
1
0..*
+featureOfInterest
1
0..*
+procedure
1
+result
An Observation is an action whose result is an estimate of the value of some property of the feature-of-interest, obtained using a specified procedure
Cox, OGC Abstract Specification – Topic 20: Observations and Measurements 2.0 ISO 19156:2011 Geographic Information – Observations and measurements

## Slide 3
Cox, OGC Implementation – Observations and Measurements - XML Implementation

## Slide 4: Why JSON?
  “So these days, if you want to interchange tuples or tables of tuples or numbers and strings, you have JSON. If you want to do nontrivial publishing automation, use XML. If you want to interchange smart bitmaps of page images, there’s PDF. I personally think we’re probably done with inventing low-level textual interchange formats.”
    Tim Bray http://www.tbray.org/ongoing/When/201x/2013/02/10/XML-at-15

## Slide 5: OM-JSON
{ "id":"measure-instance-test", "type" : "Measurement", "phenomenonTime": { "instant":"2011-05-11T00:00:00+10:00" }, "observedProperty": {"href":"http://environment.data.gov.au/def/property/air_temperature"}, "procedure": {"href":"http://www.opengis.net/def/waterml/2.0/processType/Sensor"}, "featureOfInterest": {"href":"http://waterml2.csiro.au/rgs-api/v1/monitoring-point/419009/"}, "resultTime": "2011-05-12T09:00:00+10:00", "result": { "value": 3.2, "uom": "http://qudt.org/vocab/unit#DegreeCelsius" } }
O&M terminology
JSON syntax

## Slide 6: OM-JSON – time-series
{ "id":"timeseries-instance-test", "type" : "http://www.opengis.net/def/observationType/OGC-OM/2.0/OM_DiscreteTimeSeriesObservation", "phenomenonTime": { "begin":"2015-08-03", "end":"2015-08-05" }, "observedProperty": {"href":"http://environment.data.gov.au/def/property/air_temperature"}, "procedure": {"href":"http://www.opengis.net/def/waterml/2.0/processType/Sensor"}, "featureOfInterest": {"href":"http://waterml2.csiro.au/rgs-api/v1/monitoring-point/419009/"}, "resultTime": "2015-08-05T09:00:00+10:00", "result": { "defaultPointMetadata": { "interpolationType": {"href": "http://www.opengis.net/def/waterml/2.0/interpolationType/Continuous"}, "uom" : "http://qudt.org/vocab/unit#DegreeCelsius" }, "points": [ { "time": { "instant": "2015-08-03" }, "value": 3.2 }, { "time": { "instant": "2015-08-04" }, "value": 3.5 }, { "time": { "instant": "2015-08-05" }, "value": 3.6 } ] } }
TimeseriesML encoding

## Slide 7: OM-JSON
{ "id":"polygon-example", "phenomenonTime": { "instant":"2011-05-11T00:00:00+10:00"}, "observedProperty": { "href":"http://environment.data.gov.au/def/property/shape"}, "procedure": { "href":"http://www.opengis.net/def/waterml/2.0/processType/Sensor"}, "featureOfInterest": { "href":"http://environment.data.gov.au/water/id/catchment/100862", "title":"Observed catchment"}, "resultTime": "2011-05-12T00:00:00+10:00", "result": { "type": "Polygon", "coordinates" : [[ [-180.0, 10.0], [20.0, 90.0], [180.0, -5.0], [-30.0, -90.0], [-180.0, 10.0] ]] } }
GeoJSON for geometry

## Slide 8: OM-JSON
{ "id": "spec1", "type": "Specimen", "sampledFeature": { "href": "http://example.org/featureA", "title": "test feature A" }, "complex": [ { "rel": "http://example.org/parent", "href": "http://example.org/sample2" }, { "rel": "http://example.org/child", "href": "http://example.org/sample3" } ], "samplingTime": { "instant": "2015-05-14" }, "relatedObservation": [ { "href": "http://example.org/obs99" } ], "samplingLocation": { "type": "Point", "coordinates": [ -30, -90 ] }, "currentLocation": { "href": "http://example.org/locations/store", "title": "bottom drawer" }, "size": { "value": 23.1, "uom": "http://www.opengis.net/def/uom/ogc/0/m" } }
Link model – href, rel, title

## Slide 9: OM-JSON
{ "id": "sampling feature collection 77", "sampledFeature": [ { "href": "http://example.org/feature45", "title": "Derwent River" } ], "member": [ { "href": "http://example.org/sample23" }, { "id": "spec56", "type": "Specimen", "samplingTime": { "instant": "2015-05-14" }, "samplingLocation": { "type": "Point", "coordinates": [ -30, -90 ] }, "size": { "value": 2, "uom": "l" } } ] }
Sampling feature collection
Members
- by-reference or in-line
- inherit common properties

## Slide 10: OM-JSON
{ "id": "observation collection a34", "phenomenonTime": { "instant":"2015-05-11" }, "featureOfInterest": { "href":"http://example.org/sighting345" }, "member": [ { "href": "http://example.org/o23" }, { "id":"o96", "type": "CategoryObservation", "observedProperty": { "href": "http://environment.data.gov.au/def/property/taxon" }, "procedure": { "href":"http://www.opengis.net/def/waterml/2.0/processType/Manual" }, "resultTime": "2015-05-12T09:00:00+10:00", "result": { "term": "johnstons-crocodile" , "vocabulary": "http://environment.data.gov.au/def/object/" } } ] }
Observation collection
Members
- by-reference or in-line
- inherit common properties

## Slide 11: JSON Schema for OM-JSON
Common types, for use in other OGC JSON encodings?
JSON-schema for TimeseriesML
Collection objects, carry common properties
No external dependencies

## Slide 12: JSON Schema and validator
Adapted version of JSON Schema Lint here: http://waterml2.csiro.au/om-json/
JSON Schema available here: http://github.com/peterataylor/om-json

## Slide 13: Issues
This encoding focuses on the information model
  How best to wrap these for use in API/Services?
  E.g. using SOS (52North), SensorThings, SensorCloud (CSIRO)
Some (minor) differences in approaches to schema inheritance and typing.
  The 52North schema are quite similar and these could be harmonised

## Slide 14: Changes required to Abstract Spec (O&M)
add samplingStrategy to Observation
  featureOfInterest used only for the feature with observed property
ObservationCollection, for common properties of member observations
  procedure, featureOfInterest, samplingStrategy, observedProperty, phenomenonTime, resultTime
add samplingElevation to Specimen
  vertical offset from a 2-D location a common requirement
SamplingFeatureCollection, for common properties of member sampling features
  sampledFeature

## Slide 15: Discussion paper
OM-JSON – OGC 15-100rN Discussion Paper has been approved for publication at OGC.

## Slide 16: Discussion points
JSON Schema?
base types for OGC JSON implementations
52North version of JSON for SOS
OM-JSON vs SensorThings
use of GeoJSON for geometry, alternatives
UMLJSON rules

## Slide 17
Land and water
Thank you
CSIRO Land and Water
  Simon Cox Research Scientist
    t +61 3 9545 2365
    e simon.cox@csiro.au
    w people.csiro.au/C/S/Simon-Cox
CSIRO Data61
  Peter Taylor Engineer
    t +61 3 6232 5530
    e peter.taylor@csiro.au
    w http://people.csiro.au/T/P/Peter-Taylor