## Slide 1: WaterML 2.0 + TimeseriesML (draft) Overview & discussion
Peter Taylor
Research Engineer, CSIRO
2012-02-01
David Arctur (updates)
Research Scientist, UT Austin
2015-09-01 for NASA ESDSWG

## Slide 2: What I’ll cover
History
Requirements and constraints
Overview of the information model
Usage
Future work & discussion

## Slide 3: The problem
Need flow data!
I’ll ring Don, he Has Data
*RING RING*
Hi Don, I need some upper Derwent flow readings for my geochemical model. Any ideas?
Don
Hmm, I’ve got one site. I’ll send it through…
10 minutes…
To: Jack
01/02/09, 3.2, 3, 1
01/02/09, 3.1, 3, 1
10 minutes…
*RING RING*
Ok. Got the data. Where is the site located?
Oh, it’s at laughing jack bridge.
Coordinates?
Ummm. (papers shuffle)
147.123 -41.588
What reference system??
I think it’s GDA94
Ok. What sensor is used?
It’s calculated from the stream gauge reading using a rating curve..
Oh…how accurate is that?
Umm......
DON?
Hydro Jack
*CLICK*

## Slide 4: A brief history
2007 – WaterML 1.0 discussion paper to Open Geospatial Consortium
2008-2009 – Discussions between CUAHSI and CSIRO for a harmonized water observations standard
2008-2009 – OGC/WMO Hydrology Domain Working Group formed
2010 – OGC Discussion paper: “Harmonizing Standards for Water Observations Data”
2011 – Formation of OGC Standards Working Group (SWG) for WaterML2.0 development
2012 – OGC adoption of WaterML2.0 international standard
(Updated Aug 2015, DArctur)

## Slide 5: OGC/WMO Hydrology Domain Working Group
2008
2009
2010
2011
2012
Hydrology Domain Working Group started
OGC at WMO Commission for Hydrology
7+ Year International Effort – WaterML
2013
2014
Technical Meetings every 3 months
Five Interoperability Experiments (Surface water, groundwater, ratings-gaugings)
Annual week-long workshops
Involvement by many countries
WML2 Part 2 Ratings-Gaugings
Acknowledgements: OGC, WMO, GRDC, NWS, CUAHSI, BoM/CSIRO, USGS, GSC, Kisters, …….
Stage-Discharge values for one cross-section
A time series for one variable at one location
(vote pending)
Memorandum of Understanding between the World Meteorological Organization and the Open Geospatial Consortium
Sensor Observation Service 2.0
Hydrology Profile
Best Practice
Notes: (1) A four-year international effort has been undertaken to reconcile WaterML with international standards;
(2) This effort was initiated with the establishment of an Hydrology Domain Working Group by the Open Geospatial Consortium in September 2008;
(3) An OGC representative attended the WMO Congress of the Commission for Hydrology in 2008
(4) A formal agreement between Secretary General of WMO and President of OGC in 2009 to jointly develop standards for hydrology, climatology, oceanography and climatology;
(5) The joint OGC/WMO Hydrology Domain Working Group was supported by a large work effort, annual week-long workshops, four interoperability experiments for surface and groundwater data exchange, and participation by many countries;
(6) In June 2012, the OGC voted to adopt the revised version, WaterML2 as an international standard for exchange of water resources time series (the first such public standard that has existed);
(7) This Congress to the WMO Commission for Hydrology to whom I am speaking is considering WaterML2 for adoption as an official standard by WMO
(8) WaterML 2.0 Part 2 – Ratings and Gagings is ready for public comment, pending OGC approval to post.

## Slide 6: Harmonization
Scope
Requirements
Design
Constraints
A new environment
Best practices
Do Stuff

## Slide 7
Requirements &
Constraints
http://spin.atomicobject.com/2012/01/26/understand-design-or-fail/

## Slide 8: Requirements & constraints
Initial scope:
  Exchange of point-based time series data
  Includes processed data such as forecasts, aggregations etc.
  Include relevant information on monitoring points, procedures and context
Working in an OGC – ISO – WMO context
  Need to re-use existing work where possible
  Be consistent
  Assist in developing existing standards if they are not sufficient
Corollary
  You need to know what the standards do and how they work

## Slide 9: Relevant standards
The Sensor Web
Web of interconnected sensors
  From micro to macro
  Enhance ‘situation awareness’
Initial concepts emerged from NASA1 (Delin et at.)
  Intraconnected sensor pods
1. http://www.sensorwaresystems.com/historical/resources/sensorweb-concept.pdf

## Slide 10: OGC’s Sensor Web
A service-based approach to providing an interoperability layer on the Web for accessing, controlling and discovering sensors
Sensor Web Enablement (SWE)

## Slide 11: SWE version 1.0
SweCommon
WNS
SOS
SAS
CS-W
TML
SensorML
O&M
Encodings
Services
SPS
Acronym heaven…
WPS
Catalog

## Slide 12: OGC (SWE) standards evolution
Acronym | Name | Status
TML | Transducer ML | 1.0. No longer developed.
O&M | Observations & Measurements | 2.0. ISO version approved.
SWE Common | Common data model | 2.0 approved.
SensorML | Sensor and process descriptions | 2.0 approved.
SAS | Sensor Alert Service* | 0.9 best practice
SPS | Sensor Planning Service | 2.0 approved.
WPS | Web Processing Service | 2.0 in progress.
CSW | Catalog Service for the Web | 2.0.2 adopted; 3.0 in progress.
WNS | Web Notification Service* | 0.9 best practice
* Sensor Event Service / OGC Eventing / PubSub SWG / WS-N. See OGC 11-088r1

## Slide 13: Common views on data
  Continuous phenomena, varying in space and time – ‘raster’.
  A function: spatial, temporal or spatio-temporal domain to attribute range
Features
  Features exist, have attributes and can be spatially described – ‘discrete’ or ‘vector’
Coverages
Observations
  An act that results in the estimation of the value of a feature property, and involves application of a specified procedure, such as a sensor, instrument, algorithm or process chain

## Slide 14: Observations & Measurements
Now ISO19156 – Observations & Measurements.
  Conceptual (UML) model
The XML encoding is OGC O&M 2.0 XML (10-025r1)
The most relevant standard within the OGC suite for WaterML2.0

## Slide 15: Where do time series fit?
OGC lacked a common definition of time series, and specifically how they relate to coverages, observations and SWE
O&M has the concept of discrete coverage observations:
  Observations where the result varies depending on spatial or temporal variation
  This links observations, coverages and features
An in-situ time series may be viewed as a spatially fixed, temporally varying coverage
  This view is consistent with netCDF (discrete sampling geometries)

## Slide 16: WaterML 2.0 overview
WaterML2.0 consists of
  Conceptual (UML) model
  XML Schema (GML compliant)
  Specification document
    Requirements
    Conformance classes
    Conformance tests
  XML Schematron rules
  Vocabulary definitions
    Only a subset relating to time series

## Slide 17: WaterML 2.0 overview
Time series structures
O&M Observation specializations (roughly a variable)
Monitoring points
Collections of monitoring points
  E.g. networks
Observation procedures
Generic collections

## Slide 18: Observation (O&M)
Feature
Phenomenon
Result
Process
Metadata
Related Observations

## Slide 19: Observation types
Time series?
Option 1:
Collection of Observation elements
Timeseries Observation
Timeseries
Option 2:
Time series as a result

## Slide 20: Coverage Observations
Interleaved timeseries (TVP)
Domain-range timeseries (TVP)

## Slide 21: XML structure
Interleaved
Domain-range

## Slide 22: Measurement timeseries
A Timeseries…
Consists of many time-value (measure) pairs…
With metadata and annotations.

## Slide 23: Timeseries metadata

## Slide 24: CodeLists (proposed for TimeseriesML)

## Slide 25: Sampling features
The domain feature is often not directly measured but estimated through a proxy, or a sampling, feature
E.g. Measuring water quality of an aquifer involves sampling at a bore or well site.
E.g. Measuring river level at a station is sampling the river at a point
Linking of sampling features to domain features allows closer interaction with GIS systems

## Slide 26: Using OGC O&M model for water level …
An Observation is an action whose result is an estimate of the value of some property of the feature-of-interest, obtained using a specified procedure
GF_PropertyType
OM_Observation
+
phenomenonTime
+
resultTime
+
validTime [0..1]
+
resultQuality [0..*]
+
parameter [0..*]
GFI_Feature
OM_Process
Any
+observedProperty
1
0..*
+featureOfInterest
1
0..*
+procedure
1
+result
Stage Height
Water level measurement
sampling feature
Stream Gage
River is a
sampled feature
Time series of values
Source: USGS
(WaterML2 Part 1)

## Slide 27: Treating rating curves as a measurement …
(Stage, Discharge) pair
GF_PropertyType
OM_Observation
+
phenomenonTime
+
resultTime
+
validTime [0..1]
+
resultQuality [0..*]
+
parameter [0..*]
GFI_Feature
OM_Process
Any
+observedProperty
1
0..*
+featureOfInterest
1
0..*
+procedure
1
+result
Gage Location
Observation or Conversion Method
sampling feature
(Stage, Discharge) tuples
Source: USGS
(WaterML2 Part 2)
An Observation is an action whose result is an estimate of the value of some property of the feature-of-interest, obtained using a specified procedure
Notes: Rating curves are developed on a planned & as-needed basis, by taking direct measurements of depth and flow, and plotting the curve from this data. The curve is then used to convert real-time measurements of depth into real-time values of discharge.
The object of WaterML 2.0 Part 2 is to apply the OGC O&M conceptual model and WaterML XML schema to convey the set of (stage, discharge) values.
Source: http://water.usgs.gov/edu/measureflow.html
See also: OGC 13-021r3 WaterML 2.0 – Part 2.

## Slide 28: The stream flow can then be determined from the rating curve
Discharge
GF_PropertyType
OM_Observation
+
phenomenonTime
+
resultTime
+
validTime [0..1]
+
resultQuality [0..*]
+
parameter [0..*]
GFI_Feature
OM_Process
Any
+observedProperty
1
0..*
+featureOfInterest
1
0..*
+procedure
1
+result
Stream Gage
Flow rate conversion
sampling feature
River is a
sampled feature
Time series of values
Source: USGS
(WaterML2 Part 1)
An Observation is an action whose result is an estimate of the value of some property of the feature-of-interest, obtained using a specified procedure
Notes: Graph source: http://waterdata.usgs.gov/nwis/uv?cb_00060=on&cb_00065=on&cb_00065=on&format=gif_default&site_no=08158000&period=&begin_date=2015-02-02&end_date=2015-02-16

## Slide 29: WaterML Web Services CUAHSI, USGS, OGC, WMO…
Water time series data on the internet
24/7/365 service
For daily and real-time data
. . . Operational water web services system for the United States
http://waterservices.usgs.gov/nwis/iv/?format=waterml,2.0&sites=08158000&period=P1D&parameterCd=00060
Notes: Increasingly, national water data is being published using WaterML to describe time series of observations and model results. This is the current output from the US Geological Survey for one of their tens of thousands of river gauges (this one is on the Colorado River in Austin TX).

## Slide 30
Putting into practice

## Slide 31: Web Services
A logical fit with OGC’s Sensor Observation Service (SOS) 2.0
May be used with other services,
  WaterOneFlow
  Generic web services
  RESTful services
Prototypes from Interoperability Experiments:
  Groundwater IE
  Surfacewater IE
  Forecasting IE
(Updated Aug 2015, DArctur)

## Slide 32: Specificity
Some parts of WaterML2.0 need further definition for particular usages
  Focus was on getting core structures defined and consistency
Best practices and related standards
  OGC Best Practice: Sensor Observation Service 2.0 Hydrology Profile
  OGC Best Practice: WaterML-WQ – an O&M and WaterML 2.0 profile for water quality data (1.0)
  WaterML 2.0 Part 2 – Ratings, Gaugings & Sections has been adopted and is in final stages of publication
OGC Hydrology Domain Working Group public wiki:
  http://external.opengis.org/twiki_public/HydrologyDWG/WebHome
(Updated Aug 2015, DArctur)

## Slide 33: Evolution
Convergence of various communities:
  GIS, ‘feature’ view
  Atmospheric, oceanographic – multi-dimensional, coverages
  Satellite/Sensor-centric view
  Hydrologists
WaterML 2.0 provides a step in the right direction for the hydro domain; TimeseriesML generalizes this for multiple domains
Given the increasingly multidisciplinary nature of science, it helps to align our ‘data world views’
  Tension between community-specific requirements and abstract, flexible models – each have their role

## Slide 34: Future work
Relationship of WaterML 3.0 (?) to TimeseriesML
NetCDF mapping (in progress; some applications exist)
Gap analysis leading to extensions &/or restrictions for satellite data
JSON, SWE Common encodings
Controlled vocabularies
Multiple variables per time series
(Updated Aug 2015, DArctur)

## Slide 35: Timeseries Profile of OGC O&M / TimeseriesML – Open Call for Public Comment
Call for Comments (closes 9-17-2015)
  Members of the Open Geospatial Consortium (OGC®) request comments on proposed OGC standards for the representation of observations as timeseries, that is, a sequence of data values which are ordered in time.
  The OGC Timeseries Profile of Observations and Measurements candidate standard is a conceptual model for the representation of observations data as timeseries, with the intent of enabling the exchange of such data sets across information systems.
  An accompanying OGC candidate standard defines an XML encoding (OGC TimeseriesML 1.0 - XML Encoding of the Timeseries Profile of Observations and Measurements). Other encodings may be developed in future.
Downloads
  Timeseries Profile of Observations and Measurements (15-043r1)
  TimeseriesML 1.0 - XML Encoding of the Timeseries Profile of Observations and Measurements (15-042r1) – includes schema

## Slide 36: Community
The Hydro & Met-Ocean Domain Working Groups
  Common problems being solved – let’s pool our resources!
  Open standards, and source, come into their own when critical mass is reached
  A governance framework linking with OGC and WMO
Temporal DWG and Timeseries SWG
Let’s grow the international community of practice for sharing time series data

## Slide 37: Thank you
CSIRO ICT Centre
Pete Taylor
Email: peter.taylor@csiro.au
Web: www.csiro.au/science/TasICTCentre.html
University of Texas at Austin
David Arctur
Email: david.arctur@utexas.edu
Notes: 37