## Slide 1: WaterML 2.0 Overview & discussion
Peter Taylor
Research Engineer, CSIRO
1st February, 2012, HIS teleconference

## Slide 2: What I’ll cover
History
Requirements and constraints
Overview of the information model
Usage
Future work & discussion

## Slide 3: The problem
Need flow data!
I’ll ring Don, he Has Data
*RING RING*
Hi Don, I need some upper Derwent flow readings for my geochemical model. Any ideas?
Don
Hmm, I’ve got one site. I’ll send it through…
10 minutes…
To: Jack
01/02/09, 3.2, 3, 1
01/02/09, 3.1, 3, 1
10 minutes…
*RING RING*
Ok. Got the data. Where is the site located?
Oh, it’s at laughing jack bridge.
Coordinates?
Ummm. (papers shuffle)
147.123 -41.588
What reference system??
I think it’s GDA94
Ok. What sensor is used?
It’s calculated from the stream gauge reading using a rating curve..
Oh…how accurate is that?
Umm......
DON?
Hydro Jack
*CLICK*

## Slide 4: A brief history
2007 – WaterML 1.0 discussion paper to Open Geospatial Consortium
2008-2009 – Discussions between CUAHSI and CSIRO: harmonized water observations standard
2009 – Formation of joint WMO-OGC Hydrology Domain Working Group
2010 – OGC Discussion paper: “Harmonizing Standards for Water Observations Data”
2011 – Formation of OGC Standards Working Group (SWG) for WaterML2.0 development
2012 – OGC call for public comment on WaterML2.0 candidate standard

## Slide 5: Harmonization
Scope
Requirements
Design
Constraints
A new environment
Best practices
Do Stuff

## Slide 6
Requirements &
Constraints
http://spin.atomicobject.com/2012/01/26/understand-design-or-fail/

## Slide 7: Requirements & constraints
Initial scope:
  Exchange of point-based time series data
  Includes processed data such as forecasts, aggregations etc.
  Include relevant information on monitoring points, procedures and context
Working in an OGC – ISO – WMO context
  Need to re-use existing work where possible
  Be consistent
  Assist in developing existing standards if they are not sufficient
Corollary
  You need to know what the standards do and how they work

## Slide 8: Relevant standards
The Sensor Web
Web of interconnected sensors
  From micro to macro
  Enhance ‘situation awareness’
Initial concepts emerged from NASA1 (Delin et at.)
  Intraconnected sensor pods
1. http://www.sensorwaresystems.com/historical/resources/sensorweb-concept.pdf

## Slide 9: OGC’s Sensor Web
A service-based approach to providing an interoperability layer on the Web for accessing, controlling and discovering sensors
Sensor Web Enablement (SWE)

## Slide 10: SWE version 1.0
SweCommon
WNS
SOS
SAS
CS-W
TML
SensorML
O&M
Encodings
Services
SPS
Acronym heaven…
WPS
Catalog

## Slide 11: OGC (SWE) standards evolution
Acronym | Name | Status
TML | Transducer ML | 1.0. No longer developed.
O&M | Observations & Measurements | 2.0. ISO version approved.
SWE Common | Common data model | 2.0 approved.
SensorML | Sensor and process descriptions | 2.0 approved.
SAS | Sensor Alert Service* | 0.9 best practice
SPS | Sensor Planning Service | 2.0 approved.
WPS | Web Processing Service | 2.0 in progress.
CSW | Catalog Service for the Web | 2.0.2
WNS | Web Notification Service* | 0.9 best practice
* Sensor Event Service / OGC Eventing / PubSub SWG / WS-N. See OGC 11-088r1

## Slide 12: Common views on data
  Continuous phenomena, varying in space and time – ‘raster’.
  A function: spatial, temporal or spatio-temporal domain to attribute range
Features
  Features exist, have attributes and can be spatially described – ‘discrete’ or ‘vector’
Coverages
Observations
  An act that results in the estimation of the value of a feature property, and involves application of a specified procedure, such as a sensor, instrument, algorithm or process chain

## Slide 13: Observations & Measurements
Now ISO19156 – Observations & Measurements.
  Conceptual (UML) model
The XML encoding is OGC O&M 2.0 XML (10-025r1)
The most relevant standard within the OGC suite for WaterML2.0

## Slide 14: Where do time series fit?
OGC lacks a common definition of time series, and specifically how they relate to coverages, observations and SWE
O&M has the concept of discrete coverage observations:
  Observations where the result varies depending on spatial or temporal variation
  This links observations, coverages and features
An in-situ time series may be viewed as a spatially fixed, temporally varying coverage
  This view is consistent with netCDF (discrete sampling geometries)

## Slide 15: WaterML 2.0 overview
WaterML2.0 consists of
  UML model
  XML Schema (GML compliant)
  Specification document
    Requirements
    Conformance classes
    Conformance tests
  XML Schematron rules
  Vocabulary definitions
    Only a subset relating to time series

## Slide 16: WaterML 2.0 overview
Time series structures
O&M Observation specializations (roughly a variable)
Monitoring points
Collections of monitoring points
  E.g. networks
Observation procedures
Generic collections

## Slide 17: Observation (O&M)
Feature
Phenomenon
Result
Process
Metadata
Related Observations

## Slide 18: Observation types
Time series?
Option 1:
Collection of Observation elements
Timeseries Observation
Timeseries
Option 2:
Time series as a result

## Slide 19: Coverage Observations
Interleaved timeseries (TvP)
Domain-range timeseries (TvP)

## Slide 20: XML structure
Interleaved
Domain-range

## Slide 21: Measurement timeseries
A Timeseries…
Consists of many time-value (measure) pairs…
With metadata and annotations.

## Slide 22: Timeseries metadata

## Slide 23: Sampling features
The domain feature is often not directly measured but estimated through a proxy, or a sampling, feature
E.g. Measuring water quality of an aquifer involves sampling at a bore or well site.
E.g. Measuring river level at a station is sampling the river at a point
Linking of sampling features to domain features allows closer interaction with GIS systems

## Slide 24: Example sampling features

## Slide 25
Putting into practice

## Slide 26: Web Services
A logical fit with OGC’s Sensor Observation Service (SOS)
  Version 2.0 is being voted on by OGC
May be used with other services,
  WaterOneFlow
  Generic web services
  RESTful services
Prototypes from Interoperability Experiments:
  Groundwater IE
  Surfacewater IE
  Forecasting IE

## Slide 27: Specificity
Some parts of WaterML2.0 will need to be defined for particular usages
  Focus was on getting core structures defined and consistency
Best practices and future iterations to come
OGC network pages a starting ground:
  http://www.ogcnetwork.net/node/1748

## Slide 28: Evolution
Convergence of various communities:
  GIS, ‘feature’ view
  Atmospheric, oceanographic – multi-dimensional, coverages
  Sensor-centric view
  Hydrologists
WaterML2.0 hopes to provide a step in the right direction for the hydro domain
Given the increasingly multidisciplinary nature of science, it helps to align our ‘data world views’
  Tension between community-specific requirements and abstract, flexible models – each have their role

## Slide 29: Future work
Interest in exchange of ratings, gaugings (and cross sections)
  Hydro DWG will be kicking off something in the space soon…
Water quality specific encodings
NetCDF mapping is in progress
JSON, SWE Common encodings
Controlled vocabularies

## Slide 30: Community
The Hydro Domain Working Group
  Common problems being solved – let’s pool our resources!
  Open standards, and source, come into their own when critical mass is reached
  A governance framework linking with OGC and WMO
Let’s grow the international community of practice for sharing water data

## Slide 31: Thank you
CSIRO ICT Centre
Pete Taylor
Phone: +61 3 6232 5530
Email: peter.taylor@csiro.au
Web: www.csiro.au/science/TasICTCentre.html
Contact Us Phone: 1300 363 400 or +61 3 9545 2176 Email: Enquiries@csiro.au Web: www.csiro.au
Notes: 31

## Slide 32
Backup slides

## Slide 33
Monitoring Point (x,y)
Proc1_2m_temp_sensor
Proc1_1m_temp_sensor
Observation 1
FeatureOfInterest=SamplingPoint1
Procedure=Proc1_1m_temp_sensor
ObservedProperty=temperature
Result=MeasureTimeseries(
01/01/01T12:00:00,2.3
01/01/01T12:00:00,2.3)
Observation 2
FeatureOfInterest=SamplingPoint1
Procedure=Proc1_2m_temp_sensor
ObservedProperty=temperature
Result=MeasureTimeseries(
01/01/01T12:00:00,1.1
01/01/01T12:00:00,1.2)
SensorSystem
FeatureOfInterest=SamplingPoint1
Procedure=Proc1_2m_temp_sensor
ObservedProperty=temperature
Result=(MeasureTimeseries
01/01/01T12:00:00,1.1
01/01/01T12:00:00,1.2)
Implications:
- Have to create a unique procedure for each series
- Height is embedded in procedure definition (e.g. sensorsML)
Multiple observations returned for GetObs(foi, obs_prop)
Result type is simple (tvp, measure)
Type #1 - Vertical in procedure

## Slide 34
SamplingPoint2 (x,y,z)
SamplingPoint1 (x,y,z)
Observation 1
FeatureOfInterest=SamplingPoint1 (x,y,1)
Procedure=temperature_sensor
ObservedProperty=temperature
Result=MeasureTimeseries(
01/01/01T12:00:00,2.3
01/01/01T12:00:00,2.3)
Observation 2
FeatureOfInterest=SamplingPoint2 (x,y,2)
Procedure=temperature_sensor
ObservedProperty=temperature
Result=(MeasureTimeseries
01/01/01T12:00:00,1.1
01/01/01T12:00:00,1.2)
Procedure=temperature_sensor
Sampling Group
member=SamplingPoint1
member=SamplingPoint2
Implications:
Have to handle 3D coordinates
May end up with a lot of sampling points
Groups of samplings points required if the relationship is to be explicitly captured (it’s naturally captured with spatial proximity and same observed property)
Can query explicitly for each sampling point
Result structure is simple (tvp, measure)
Type #2 – 3D coordinates

## Slide 35
SamplingPoint1 (x,y)
procedure=temp_sensor
procedure=temp_sensor
Observation 1
FeatureOfInterest=SamplingPoint1
Parameter={verticalHeight=1m}
Procedure=temp_sensor
ObservedProperty=temperature
Result=MeasureTimeseries(
01/01/01T12:00:00,2.3
01/01/01T12:00:00,2.3)
Observation 2
FeatureOfInterest=SamplingPoint1
Parameter={verticalHeight=2m}
Procedure=temp_sensor
ObservedProperty=temperature
Result=(MeasureTimeseries
01/01/01T12:00:00,1.1
01/01/01T12:00:00,1.2)
Implications:
A generic procedure type is used
Cannot query for vertical height natively (without extension)
No site specific procedure information can be provided
Multiple observations returned for a site: client needs to understand why they are different
Type #3 – Observation metadata

## Slide 36
SamplingPoint1 (x,y)
procedure=temp_sensor
procedure=temp_sensor
Composite Observation
FeatureOfInterest=SamplingPoint1
Procedure=temp_sensor
ObservedProperty=CompoundProperty
Result=MeasureTimeseries(
01/01/01T12:00:00,2.3,1.0
01/01/01T12:00:00,2.3,2.0
01/01/01T12:00:00,2.2,1.0
01/01/01T12:00:00,2.2,2.0 )
Vertical offset
Implications:
A generic procedure type is used
Querying for vertical height would require a result filter (vertical height not first class)
No site specific procedure information can be provided
Single observation returned for site.
Result type is more complex (tvp, measure, height)
Type #4 – Height as timeseries

## Slide 37
SamplingPoint1 (x1,y1)
- Right bank
SamplingPoint2 (x2,y2)
- Left bank
SamplingCollection
- SamplingPoint1
- SampingPoint2
SamplingPoint1 (x1,y1)
Observation 1
FeatureOfInterest=SamplingPoint1
Procedure=level_sensor
OObservedProperty=gage height, stream
Result=CompositeTimeseries(
01/01/01T12:00:00,2.3, Left
01/01/01T12:00:00,2.3, Right
)
Bank identifier
Unknown location
Observation 2
FeatureOfInterest=SamplingPoint2
Procedure=level_sensor
ObservedProperty=gage height, stream
Result=MeasureTimeseries(
01/01/01T12:00:00,2.3
01/01/01T14:00:00,2.4)
Observation 1
FeatureOfInterest=SamplingPoint1
Procedure=level_sensor
ObservedProperty=gage height, stream
Result=MeasureTimeseries(
01/01/01T12:00:00,2.3
01/01/01T14:00:00,2.4)
Same example holds for upstream/downstream sensors where they are both part of the same ‘site’ and coordinates may not be known.
Measuring on either side of river bank

## Slide 38: Integrating with Hydrologic Features
“Sampled Feature” is not always obvious
Use cases of real locations, raw data streams processing and delivered data products
  Use domain scientists to extract implied information to sampled features.

## Slide 39
SamplingPoint1 (x2,y2)
-
Sensor1 (x2,y2)
-Upstream
Observation 2
FeatureOfInterest=SamplingPoint
Parameter={downstream}
Procedure=level_sensor
ObservedProperty=gage height, stream
Result=MeasureTimeseries(
01/01/01T12:00:00,2.3
01/01/01T14:00:00,2.4)
Observation 1
FeatureOfInterest=SamplingPoint1
Parameter={upstream}
Procedure=level_sensor
ObservedProperty=stage ,stream
Result=MeasureTimeseries(
01/01/01T12:00:00,2.3
01/01/01T14:00:00,2.4)
Same sampling feature, but multiple sensors may be observing a different sampled feature
Measuring upstream and downstream
Weir
sensor2 (x2,y2)
-downstream

## Slide 40
SamplingPoint1 (x2,y2)
-
Observation 2
FeatureOfInterest=SamplingPoint1
Procedure=Dsscharge sensor
InterpoloationType=Preceeding Average
Period=15 min
ObservedProperty=Discharrge, stream
Result=MeasureTimeseries(
01/01/01T12:00:00,2.3
01/01/01T14:00:00,2.4)
Observation 1
FeatureOfInterest=SamplingPoint1
Procedure=level_sensor
InterpoloationType=Preceeding Average
Period=15 min
ObservedProperty=Gauge Hieight
Result=MeasureTimeseries(
01/01/01T12:00:00,2.3
01/01/01T14:00:00,2.4)
Tidally influence filtered
SamplingPoint1 (x1,y1)
Observation 1
FeatureOfInterest=SamplingPoint1
Procedure=72137 Discharge, ltide ftrd(Mean)
IntepolationType=Succeeding Average
Period=1 day
OObservedProperty=Discharge,
Result=CompositeTimeseries(
01/01/01T12:00:00,2.3,
01/01/01T12:00:00,2.3,
)
Processing
Observation 2
FeatureOfInterest=SamplingPoint1
Procedure=Velocity sensor
InterpoloationType=Preceeding Average
Period=15 min
ObservedProperty=Veliocity, stream
Result=MeasureTimeseries(
01/01/01T12:00:00,2.3
01/01/01T14:00:00,2.4)
Processed - Daily Average
Raw Data – 15 minute average