## Slide 1: Building a Water Intelligence Network Using Hydro Network Linked Data
Al Rea
Dave Blodgett
June 15, 2017

## Slide 2: Overview
NHDPlus V2 (Medium Resolution)
NHDPlus HR
HydroLink, HEM, and ScienceBase
Services for network-based search (NLDI)

## Slide 3: National Hydrography Dataset Plus - NHDPlus
Medium Resolution created for CONUS
High Resolution in work for CONUS and AK
Incorporates
  Hydrography
  Boundaries
  Elevation
NHD
WBD
Elevation

## Slide 4: Catchments
Notes: Here is a picture of some catchments. You can see there is a catchment for each line segment in the NHD network. There are catchments for each coastal line segment, too. The catchments in NHDPlus cover the entire continental US. If you drop a hypothetical drop of water anywhere in the 48 states, you can know instantly where in the stream network that drop of water would go simply by intersecting the point where it falls with the catchment dataset.

## Slide 5: NHDPlusHR
The best of 24K+ data and NHDPlus
Addresses the need for a single hydrographic frame of reference
Link data to one network and generalize to many different scales
Taking NHDPlus v2 (MedRes) to a new level
NHD
100K
2000
NHD HR
24K
Local/State
applications
2007
NHDPlus
High Resolution
Local/State applications AND scalable applications
Started 2015
NHDPlus
100K
Regional/National applications
2006

## Slide 6: NHD Data Suite Comparison
 | NHDPlus v2 (Med Res) | NHDPlus - High Res
Number of features | 3 Million nationally | 26 Million nationally
Elevation Input | National 1 Arc-Second Seamless DEM (30 meters) | National 1/3 Arc-Second Seamless DEM (10 meters)
NHD Input | Medium Resolution NHD 100K | High Resolution NHD 24K - Local
WBD Input | Composite 2010-2012 | Updated WBD
Tile size | HUC-2 (with exceptions) (avg. XX square miles) | HUC-4 (avg. XX square miles)
Flow estimates | Mean annual, mean monthly | Mean annual
Component Datasets
NHDPlus (both resolutions) is made from the combination of elevation data, hydrography data (NHD), and watershed boundaries (WBD)
NHDPlusHR uses higher resolution input data
Notes: NHD+ is combination of NHD, WBD, and elevation
NHD – no WBD, no elevation
HUC2 – couple hundred square miles
HUC4 – 20k square miles
NHD+HR does NOT use 3dep at native resolution – has to downgrade to 10m
Features increased 3M in NHD+ to 33M in NHD+HR
Catchment size decreased from 2 sq. mi. to 2/10 of square mile

## Slide 7
Notes: Note two focuses 1. Data Availability, 2. Partner / User Engagement
25% CONUS HU4s available… 40% by end of FY
Blue areas - NHDPlus HR Beta is currently available and review/QC may be in process. Please see the NHDPlus HR Beta review/QC section below for more information.
Green areas - NHDPlus HR Beta will be produced at a later date. Please see the general processing schedule below for more information. These areas are currently open for NHD and WBD editing.
Orange areas - The NHD and WBD in these areas are being prepared for NHDPlus HR production and are closed for NHD and WBD editing.
Yellow areas - The USGS is seeking volunteers to for the NHDPlus HR Beta review/QC for these areas. Please see the NHDPlus HR Beta review/QC section below for more information. Please contact the NHD Point of Contact in your area for more information on the status of NHD and WBD editing in these areas.

## Slide 8: NHDPlusHR Current Processing Order
WBD HU2, HU4, or HU6 | Hydrologic Region | Additional Information | # of HU4s
06 | Tennessee | Mississippi 1 of 6 | 4
01 | Northeast |  | 10
12 | Texas |  | 11
14 | Upper Colorado | Colorado 1 of 2 | 8
15 | Lower Colorado | Colorado 2 of 2 | 8
02 | Mid-Atlantic |  | 6
16 | Great Basin |  | 6
0903 | Canadian Pilot (0903) | Pilot (Rainy River Lake of the Woods) | 1
10 | Missouri | Mississippi 2 of 6 | 29
07 | Upper Mississippi | Mississippi 3 of 6 | 14
041504 | Canadian Pilot (041504) | Pilot (Lake Champlain) | 1
05 | Ohio | Mississippi 4 of 6 | 14
09 | Souris, Red, Rainy | Souris, Red, Rainy (less pilot) | 3
1902 | Alaska Pilot (1902) | Pilot (MatSu) | 1
11 | Arkansas, Red, White | Mississippi 5 of 6 | 14
1801 | Klamath River Basin | Klamath Dam Removal Project | 1
3 | South Atlantic |  | 18
17 | Pacific Northwest | Pacific Northwest | 12
13 | Rio Grande |  | 9
4 | Great Lakes | Complete Drainage Area (less pilot) | 15
8 | Mississippi | Mississippi 6 of 6 | 9
18 | California | California (less Klamath Priority) | 9
19 | Alaska | Alaska (less MatSu Pilot) | -
20 | Hawaii | - | -
21 & 22 | Virgin Islands & Puerto Rico | - | -
Italicized text indicates partial subregion (HU4). |  |  | 
Notes: This is our current program of work (not necessarily in priority order), there were a number of considerations in determining this sequence
This sequence represents A. start with some successes, Region 06, good opportunity for us to start, B. wanted to ensure we could complete connected networks with the upper and lower colorado, so by the time we got to the Mississippi we knew our process would work in more complex areas C. Coastal data in Region 1
This gave other priority areas, such as California to prepare the source data for NHDPlus HR
We knew there would be some challenges in areas such as the great lakes, so we focused on some other areas first to stabilize the process
Items shown in Blue represent the FY16 program of work, the following colors represent our current and future plans, including pilots in Alaska and Canada
Also found on NHD website

## Slide 9: Markup Application
Web Application
Desktop Application - ArcGIS Add-on
Users: public, non-trained NHD and WBD editors, academia, etc.
Purpose:
Viewing NHD and WBD layers, and submitting markups
Creating new markups
Users: Internal NGTOC editors, trained NHD and WBD partners only
Purpose:
View markups submitted through web application
Update markup status: resolved, won’t fix, in progress

## Slide 10
NHDPlus
NHD
WBD
3DEP
App
Water Quality Portal
HydroLink
App
Water Intelligence Network System (WINS)
Example Apps:
National Water Model
HydroLink
SPARROW
StreamStats
National Water Census
etc.
Wetlands
net-
work navi-
gation
Linked Data
Registry
etc.
App
Levees
Dams
Water Quality
STORET
NWIS
Fish
Fish locations
API
ser-
vices
Notes: Locations such as fish sampling locations are input to HydroLink, which makes calls to the API to link to the NHDPlus geospatial framework.

## Slide 11: Stream Addresses are like street addresses
100
0
50
75
25
14010002000421

## Slide 12: HU codes are like ZIP codes

## Slide 13: Linking Data Online
HydroLink Tool

## Slide 14: Linking Data to NHD
Hydrography Event Management (HEM) Tool
  Desktop ArcGIS tool
  Point, Line, Area “Events” (hydro linked data)
  Batch mode
  “Sync” of events linked to NHD Flowlines that have been edited
“Built in events” in NHD
  Dams
  HUC-8 outlets
  Streamgages
  Water Quality Stations
USGS ScienceBase for sharing linked data
  “NHD Linked Data Registry“
  Can host linked data services
  Can reference your linked data services
  Contact mdtinker@usgs.gov for info

## Slide 17
Notes: NHDPointEvent As of 7/1/2016

## Slide 21: Network Linked Data Index Use Cases
Network Master Tools: As a system manager responsible for data connected to the river network, I need a way to register my data with the index, so the network swimmer can index my data.
Actors: Person responsible for network linked data, external content management system. Information: Network linked data owner provides the system with various metadata elements as well as network linked data or metadata pointing to a supported service. The system saves this information into a content management system. Computation: The network master tools perform verifications that ensure the information passed in is sufficient and valid.
Network Swimmer: As the network linked data index system user, I need the system to ‘swim’ registered network linked data on a regular basis and update the index accordingly, so the content is correct and current.
Actors: Network linked metadata store and data. Information: The network swimmer retrieves metadata for each registered data source. Computation: If data from a given datasource is non-static or has been changed since last checked, the network swimmer retrieves data and incorporates it into the current index.
Network Linked Data Services: As a user of network linked data, I need a service that allows me to search for network linked data, so I can find my own and others’ data on the network.
Actors: Network linked data clients / users. Information: An external application passes in a stream reach or a location near a river and additional information to configure the desired features and other characteristics of the request. Computation: The network linked data service traverses the network according to the passed-in query, performs the query and formats the result to send back to the user.

## Slide 22: Water Quality Data Discovery
Using the Hydro-Network Linked Data Index

## Slide 23: Water Quality Data Discovery
Using the Hydro-Network Linked Data Index

## Slide 24: Water Quality Data Discovery
Using the Hydro-Network Linked Data Index

## Slide 25: Network Linked Data System Use Case Diagram
Network Linked Data Index System
Network Swimmer
Client Applications
Network Linked Data Services
Network Linked Data Source (WQP, etc.)
Network Master Tools
ScienceBase Content Management System
System Manager
(WQP manager)

## Slide 26: Network Linked Data System Use Case Diagram
Network Linked Data Index System
Network Swimmer
Client Applications
Network Linked Data Services
Network Linked Data Source (WQP, etc.)
Network Master Tools
ScienceBase Content Management System
System Manager
(WQP manager)
Register
Index
Search

## Slide 27: Network Linked Data System Use Case Diagram
Network Linked Data Index System
Network Swimmer
Client Applications
Network Linked Data Services
Network Linked Data Source (WQP, etc.)
Network Master Tools
ScienceBase Content Management System
System Manager
(WQP manager)
Register
Index
Search
Create
Serve
Curate
Use

## Slide 28
NHDPlus
NHD
WBD
3DEP
App
Water Quality Portal
HydroLink
App
Water Intelligence Network System (WINS)
Example Apps:
National Water Model
HydroLink
SPARROW
StreamStats
National Water Census
etc.
Wetlands
net-
work navi-
gation
Linked Data
Registry
etc.
App
Levees
Dams
Water Quality
STORET
NWIS
Fish
Fish locations
API
ser-
vices
Create
Serve
Index
Search
Register
Curate
Use
Notes: Locations such as fish sampling locations are input to HydroLink, which makes calls to the API to link to the NHDPlus geospatial framework.

## Slide 29: How can we all contribute?
Create: HydroLink, HEM, ??
Curate: ScienceBase, ??
Register: ??
Serve: WQP, NWIS, ScienceBase, ??
Use: WQP, StreamStats, R-Script, General User GUI??
Index: Point in catchment, reach code / measure, ??
Search: Navigate, ??
More linked datasets; compelling user stories

## Slide 30: Take-away points
Geospatial Hydrographic Framework
  NHDPlus at its core, provides services for many applications
  NHDPlus V2 - now
  NHDPlus HR - future
NLDI
  App using the Framework: Water Quality Portal
  Flexible index, services, data discovery.
Additional data and services
  Catchment boundaries and characteristics.
  Streamflow observations and modeling.
  Streamflow statistics and analysis tools.

## Slide 31: Resources/Links
NHDPlus V2
  services in a web map: http://arcg.is/2cRsjgK
  national seamless gdb: https://www.epa.gov/waterdata/nhdplus-national-data
NHDPlus HR info: https://nhd.usgs.gov/NHDPlus_HR.html
NLDI: https://cida.usgs.gov/nldi/about
https://owi.usgs.gov/blog/nldi-intro/
WQP: https://www.waterqualitydata.us/

## Slide 32: Extra Slides
Following slides are for possible reference, if needed

## Slide 33: VisibilityFilter - Scale Representation
Available for Region 1 and 6
Provides filtering of vector features at 8 approximate scales.
Coded-values indicate that the feature is appropriate for use at approximately the defined scale and all larger scales.
Available for NHDFlowline, NHDWaterbody, NHDArea, and NHDLine feature classes.
Notes: Ariel / Ryan
The VisibilityFilter attribute currently is in a testing phase. VisibilityFilter attribute population will be updated to become an automated process prior to NHDPlus HR creation. The new process will allow the VisibilityFilter attribute to be populated on NHD source data, NHDPlus HR data and when a geometry change to any of the NHD feature classes with the VisibilityFilter attribute is detected, ensuring NHD and NHDPlus HR data VisibilityFilter attributes are maintained and current.

## Slide 34: Sample Data
Batch Pruning NHD Data to Smaller Scales, Stauffer, A. J., Finelli E. L., Stanislawski J.V.

## Slide 35: Sample Data
Batch Pruning NHD Data to Smaller Scales, Stauffer, A. J., Finelli E. L., Stanislawski J.V.

## Slide 36: Sample Data
Batch Pruning NHD Data to Smaller Scales, Stauffer, A. J., Finelli E. L., Stanislawski J.V.

## Slide 37: Sample Data
Batch Pruning NHD Data to Smaller Scales, Stauffer, A. J., Finelli E. L., Stanislawski J.V.

## Slide 38: Sample Data
Batch Pruning NHD Data to Smaller Scales, Stauffer, A. J., Finelli E. L., Stanislawski J.V.

## Slide 39
Batch Pruning NHD Data to Smaller Scales, Stauffer, A. J., Finelli E. L., Stanislawski J.V.

## Slide 40
Batch Pruning NHD Data to Smaller Scales, Stauffer, A. J., Finelli E. L., Stanislawski J.V.

## Slide 41: Transition from NHDPlus V2 to NHDPlus HR
How/when does this happen?
What are key requirements before this can happen?
Pilots?

## Slide 42: NLDI NWIS Site
https://cida.usgs.gov/nldi/nwissite/USGS-02465000

## Slide 43
https://cida.usgs.gov/nldi/nwissite/USGS-02465000/navigate/UT https://cida.usgs.gov/nldi/nwissite/USGS-02465000/navigate/UT/wqp https://cida.usgs.gov/nldi/nwissite/USGS-02465000/basin https://cida.usgs.gov/nldi/nwissite/USGS-02465000/navigate/DM

## Slide 44: Gold King Mine Spill ICWater Preliminary Results
Gold King Mine
Slide courtesy of Bill Samuels, Leidos
Notes: Preliminary ICWater results provided by William B. Samuels, samuelsw@leidos.com

## Slide 45
Gold King Mine
Lake Powell
ICWater QuickTrace – 8 day travel time
ICWater Preliminary Results: Slide courtesy of Bill Samuels, Leidos
Notes: Preliminary ICWater results provided by William B. Samuels, samuelsw@leidos.com

## Slide 46
https://cida.usgs.gov/nldi/huc12pp/140801040102/navigate/DD/wqp?distance=500
(WQP sites 500 km downstream of Gold King Mine)